## Slide 1
EPICS 7
Matej Sekoranyja, Marty Kraimer, Michael Davidsaver, Ralph Lange, Andrew Johnson, Timo Korhonen, Heinz Junkes, Patrick Marschalik, Murali Shankar, Bruno Martins, Kunal Shroff, Arman Arkilic, Michael Dalesio, Anton Metzger, Greg White, David Hibkin, Guobao Shen, Sinesa Veseli, Bob Dalesio, Steve Hartman

## Slide 2: EPICS 7 Outline
EPICS 7 Introduction
Status
Services Support Application Development
Community Use
Conclusions

## Slide 3: Why EPICS 7
Integrate all data into microservices: real time, processed, and configuration.
Support services for data acquisition, data management, and analysis.
Contine to provide regular data types for common clients
Provide the ability to define arbitrary data structures for more complex data sets.
Continue to provide these capabilities in a robust, high performance environment.

## Slide 4: What Is EPICS 7 (not)
EPICS 7 is not a replacement for V3
EPICS 7 does not introduce a new IOtC database
EPICS 7 does not require you to rewrite all your drivers
EPICS 7 does not break existing systems

## Slide 5: What is EPICS 7
EPICS 3 is a set of tools, libraries and applications to create a distributed control system with IOtCs that have always been able to identify all fields of all records to other devices.
EPICS 7 extends V3, enabling other data stores to expose their data to other devices. It does not require upgrading any of your applications.
EPICS 7 adds structured data and RPC services to EPICS V3

## Slide 6: EPICS 7 Improves EPICS V3
Structured data: Extending the scope of EPICS from I&C to data acquisition, image processing, and beyond
Efficient network transfer: High performance archiving and image transfer
RPC type services: Service oriented architecture: archiver, snapshot, database backends
Complex control: Communicating with devices (groups of PVs on an IOC) in an always-consistent, transaction type way

## Slide 7: EPICS 7 Supports Structured data
V4 can do everything V3 can do (but better): Can construct pvData structures analogous to DBR types. For example the equivalent of a DBR_TIME_DOUBLE would be the structure:
NTScalar
double value
alarm_t alarm
int severity
int status
string message
time_t timestamp
long secondsPastEpoch
int nanoseconds
int userTag

## Slide 8: EPICS 7 Provides Efficient network transfer
pvAccess operations only send deltas on the wire. So if the value of the structure in the above example is modified to:
NTScalar
double value 8.1
alarm_t alarm
int severity 2
int status 3
string message HIHI_ALARM
time_t timeStamp
long secondsPastEpoch 1460589145
int nanoseconds 588698520
int userTag 0
only changed values (in bold) need be sent, plus a bitset indicating which fields have changed value.

## Slide 9: EPICS 7 Supports RPC type services
RPC type services can use structures that are different for every call and different for put (request) and get (response). pvData can encode more complex data types like a table:
NTTable
string[] labels [value, seconds, nanoseconds, status, severity]
structure value
double[] value [ 1.1, 1.2, 2.0]
long[] secondsPastEpoch [1460589140, 1460589141, 1460589142]
int[] nanoseconds [ 164235768, 164235245, 164235256]
int[] severity [ 0, 0, 1]
int[] status [ 0, 0, 3]

## Slide 10: EPICS 7 Base Status
Build System builds EPICS 3 and pvAccess into the single EPICS 7 Release
pvAccess and pvData run alongside of Channel Access and DBR_types
pvData supports structured data
NTypes are standard pvData for DBR_types, Tables, N-D Arrays, Heterogeneous Arrays, etc..
pvAccess provides improved metadata for the IOC Database
pvAccess provides communication to Relational DB and No SQL DB Services
pvAccess Gateway Alpha Release
pvAccess Database Links (2018 Q2)
Access Security (Not Yet Scheduled)
Data Aggregation is planned for Java Client API (2018 Q2)
Data Aggregation is planned for C++ Client API (Not Yet Scheduled)
EPICS Records To Take Advantage of NTYpes (Not Yet Scheduled)

## Slide 11: EPICS 7 Standard Service Status
Standard Services are developed to demonstrate the use of these mechanisms:
IOC (QSRV) 2017, Q3
areaDetector 2017, Q1
Directory 2017, Q3
Save Sets 2017, Q3
Data Index 2017, Q3
Archive 2018, Q2
Log Book 2018, Q2
Snap Shot 2018, Q2
Alarm Not Yet Specified
Unit Tests and Performance Tests are provided with most code
Python, Matlab, C++, and Java APIs available for client and service development

## Slide 12: Standard Clients Connect to Services Large and Small
IOC
Directory
I to Field
NoSQL
Instrumentation
NoSQL
CSStudio
Python, C++, Java
Configuration
Data Archive
Archive
E Log
NoSQL
Data Set
Snap Shot Data Set
HDF5
Data Index
Index Data Set
NoSQL

## Slide 13: Standard Clients Connect to Services Large and Small
IOC
Directory
I to Field
NoSQL
Instrumentation
NoSQL
CSStudio
Python, C++, Java
Configuration
Data Archive
Archive
E Log
NoSQL
Data Set
Snap Shot Data Set
HDF5
Data Index
Index Data Set
NoSQL

## Slide 14: Micro Services Support Application Development – Name Mapping
IOC
Directory
NoSQL
Instrumentation
Feedback Control
Physics Code Receives EPICS PV Names
Given Physics Device and Properties
From a Directory Service
E Log
NoSQL
Data Archive
Archive
I to Field
NoSQL

## Slide 15: Micro Services Support Application Development – Read Instrumentation
IOC
Directory
I to Field
NoSQL
Instrumentation
NoSQL
Feedback Control
Physics Code Reads All Set points and Readbacks to Calculate Errors
Errors are used to Calculate New Field Settings for Magnets
E Log
NoSQL
Data Archive
Archive

## Slide 16: Micro Services Support Application Development – Conversion Service
IOC
Directory
I to Field
NoSQL
Instrumentation
NoSQL
Feedback Control
Physics Code Sends Designed Field Setting to Conversion Service
and Receives New I Settings
E Log
NoSQL
Data Archive
Archive

## Slide 17
IOC
Directory
I to Field
NoSQL
Instrumentation
NoSQL
Feedback Control
Physics Code Sends New Current Setting
to Magnet Power Supply
E Log
NoSQL
Data Archive
Archive
Micro Services Support Application Development – Write Instrumentation

## Slide 18
IOC
Directory
I to Field
NoSQL
Instrumentation
NoSQL
Feedback Control
Physics Code Records the Activity Into Official Logbook
Lists all PVs used
E Log
NoSQL
Data Archive
Archive
Micro Services Support Application Development – Electronic Log Book

## Slide 19: Who is using EPICS 7 at this time?
ESS plans to deploy a full scale EPICS 7 control system
NSLS-II/FRIB/RAON: middle-layer services using structured data
  In production: Channel Finder, MASAR service for save sets, Data Index
  More services planned (archiver, snapshot data, elog, ...)
SNS Beamlines: implementing next generation of controls and data acquisition
LCLS I/LCLS II: re-implementing all high-level physics database access using pvAccess and middle-layer services
FHI: using archiver appliance with pvAccess and structured data
APS: uses v4 RPC services for large buffer transfer
Diamond/NSLS-II: transferring areaDetector images across the network / between processes using pvAccess
  Using >90% of physical bandwidth on 10Gb ethernet (no compression)

## Slide 20: Conclusions
EPCS 7 enables the integration of all data through microservices
Normative Types is Set of well-defined containers for generic clients
Standard microservices exist for integrating standard data stores
EPICS 7 continues to provide a robust, high performance network protocol and data interface.
Instrumentation continues to be easily configured and integrated
EPICS 7 is in use for physics applications and DAQ at multiple sites..